## Slide 1
Assembly Language Programs
8085 Microprocessor
A visual restyle of the original notes. Program text, comments, and explanations are unchanged.
Codes · Complements · Arithmetic · Sign & Parity checks
8085 Microprocessor Programs · Original code unchanged
1 / 24

## Slide 2
Contents
Programs included in this deck
01
1's and 2's complement
8-bit and 16-bit numbers
02
Square of an 8-bit number
Repeated addition using H-L
03
Factorial of a number
Subroutine multiply by repeated add
04
Multiply two 8-bit numbers
Using logical rotate instructions
05
Add two 16-bit numbers
Low byte ADD, high byte ADC
06
Positive or negative number
Sign bit via RAL and carry
07
Odd or even number
LSB via RAR and carry
08
Subtract two 8-bit numbers
With or without borrow
8085 Microprocessor Programs · Original code unchanged
2 / 24

## Slide 3
PROGRAM 01
1's , 2's complement of 8 bit number
Followed by 1's and 2's complement of 16 bit number
8085 Microprocessor Programs · Original code unchanged
3 / 24

## Slide 4
1's , 2's complement of 8 bit number
Code
8-bit · original listing
1'S COMPLEMENT
LDA C050H
CMA
STA C051H
HLT
2'S COMPLEMENT
LDA C050H
CMA
INR A
STA C051H
HLT
8085 Microprocessor Programs · Original code unchanged
4 / 24

## Slide 5
1's , 2's complement of 16 bit number
1'S COMPLEMENT
16-bit · 1'S COMPLEMENT · original listing
1'S COMPLEMENT
LXI H C050H
MOV A M
CMA
STA CO52H
INX H
MOV A M
STA C053H
HLT
8085 Microprocessor Programs · Original code unchanged
5 / 24

## Slide 6
1's , 2's complement of 16 bit number
2'COMPLEMENT
16-bit · 2'COMPLEMENT · original listing
2'COMPLEMENT
LXI H C050H
MVI B 00H
MOV A M
CMA
ADI 01H
STA C052H
JNC LOOP
INR B
LOOP LXI H C051H
MOV A M
CMA
ADD B
STA C053H
HLT
8085 Microprocessor Programs · Original code unchanged
6 / 24

## Slide 7
PROGRAM 02
8085 program to find square of a 8 bit number
8085 Microprocessor Programs · Original code unchanged
7 / 24

## Slide 8
8085 program to find square of a 8 bit number
code
original listing with addresses
2000 MVI H 20 H <- 20
2002 MVI L 50 L <- 50
2004 MVI A 00 A <- 00
2006 MOV B, M B <- M
2007 ADD M A <- A + M
2008 DCR B B <- B – 01
2009 JNZ 2007 Jump if ZF = 0
200C STA 3050 M[3050] <- A
200F HLT END
8085 Microprocessor Programs · Original code unchanged
8 / 24

## Slide 9
8085 program to find square of a 8 bit number
Explanation – Registers used A, H, L, B and indirect memory M:
Explanation
MVI H 20 – initialize register H with 20
MVI L 50 – initialize register L with 50
MVI A 00 – initialize accumulator A with 00
MOV B, M – moves the content of memory location which is indirectly specified by M in register B
ADD M – add the content of memory location which is indirectly specified by M in accumulator A
DCR B – decrement value of register B by 1
JNZ 2007 – jump to memory location 2007 if ZF = 0, i.e register B does not contain 0
STA 3050 – stores value of A in 3050
HLT – stops executing the program and halts any further execution
8085 Microprocessor Programs · Original code unchanged
9 / 24

## Slide 10
PROGRAM 03
8085 program to find the factorial of a number
8085 Microprocessor Programs · Original code unchanged
10 / 24

## Slide 11
8085 program to find the factorial of a number
code
original listing
2000H Data Data Byte
2001H Result Result of factorial
2002H LXI H, 2000H Load data from memory
2005H MOV B, M Load data to B register
2006H MVI D, 01H Set D register with 1
2008H FACTORIAL CALL MULTIPLY Subroutine call for multiplication
200BH DCR B Decrement B
200CH JNZ FACTORIAL Call factorial till B becomes 0
200FH INX H Increment memory
2010H MOV M, D Store result in memory
2011H HLT Halt
2100H MULTIPLY MOV E, B Transfer contents of B to C
2101H MVI A, 00H Clear accumulator to store result
2103H MULTIPLYLOOP ADD D Add contents of D to A
2104H DCR E Decrement E
2105H JNZ MULTIPLYLOOP Repeated addition
2108H MOV D, A Transfer contents of A to D
2109H RET Return from subroutine
8085 Microprocessor Programs · Original code unchanged
11 / 24

## Slide 12
8085 program to find the factorial of a number
Explanation
Explanation
First set register B with data.
Set register D with data by calling MULTIPLY subroutine one time.
Decrement B and add D to itself B times by calling MULTIPLY subroutine as 4*3 is equivalent to 4+4+4 (i.e., 3 times).
Repeat the above step till B reaches 0 and then exit the program.
The result is obtained in D register which is stored in memory
8085 Microprocessor Programs · Original code unchanged
12 / 24

## Slide 13
PROGRAM 04
8085 program to multiply two 8 bit numbers using logical instructions
8085 Microprocessor Programs · Original code unchanged
13 / 24

## Slide 14
Multiply two 8 bit numbers using logical instructions
code
original listing
MVI B 05 B <- 05
MVI C 04 C <- 04
MOV A, B A <- B
RLC rotate the content of A without carry
RLC rotate the content of A without carry
STA 3050 3050 <- A
HLT End of the program
Explanation
MVI B 05: assign the value 05 to B register.
MVI C 04: assign the value 04 to C register.
MOV A, B: move the content of register B to register A.
RLC: rotate the content of accumulator left without carry.
RLC: rotate the content of accumulator left without carry.
STA 3050: store the content of register A at memory location 3050
HLT: stops the execution of the program.
8085 Microprocessor Programs · Original code unchanged
14 / 24

## Slide 15
PROGRAM 05
8085 program to add two 16 bit numbers
8085 Microprocessor Programs · Original code unchanged
15 / 24

## Slide 16
8085 program to add two 16 bit numbers
code
original listing
LDA 2050 A ← 2050
MOV B, A B ← A
LDA 2052 A ← 2052
ADD B A ← A+B
STA 3050 A → 3050
LDA 2051 A ← 2051
MOV B, A B ← A
LDA 2053 A ← 2053
ADC B A ← A+B+CY
STA 3051 A → 3051
HLT Stops execution
Explanation:
LDA 2050 stores the value at 2050 in A (accumulator).
MOV B, A stores the value of A into the B register.
LDA 2052 stores the value at 2052 in A.
ADD B add the contents of B and A and store them in A.
STA 3050 stores the result in memory location 3050.
LDA 2051 stores the value at 2051 in A.
MOV B, A stores the value of A into the B register.
LDA 2053 stores the value at 2053 in A.
ADC B adds the contents of B, A, and carry from the lower bit addition and store in A.
STA 3051 stores the result in memory location 3051.
HLT stops execution.
8085 Microprocessor Programs · Original code unchanged
16 / 24

## Slide 17
PROGRAM 06
Wearher a number is positive or negative
8085 Microprocessor Programs · Original code unchanged
17 / 24

## Slide 18
Wearher a number is positive or negative
Code
original listing
LXI H C050H
MOV A M
RAL
JC LOOP
MVI A 00H
STA C053H
HLT
LOOP MVI A 01H
STA C053H
HLT
8085 Microprocessor Programs · Original code unchanged
18 / 24

## Slide 19
PROGRAM 07
To find weather the number is odd or even
8085 Microprocessor Programs · Original code unchanged
19 / 24

## Slide 20
To find weather the number is odd or even
Code
original listing
LDA C050H
RAR
JC LOOP
MVI A 00H
STA C055H
HLT
LOOP MVI A 01H
STA C055H
HLT
8085 Microprocessor Programs · Original code unchanged
20 / 24

## Slide 21
PROGRAM 08
8085 program to subtract two 8-bit numbers with or without borrow
8085 Microprocessor Programs · Original code unchanged
21 / 24

## Slide 22
Subtract two 8-bit numbers with or without borrow
code
original listing
MVI C, 00 [C] <- 00
LHLD 2500 [H-L] <- [2500]
MOV A, H [A] <- [H]
SUB L [A] <- [A] – [L]
JNC 200B Jump If no borrow
INR C [C] <- [C] + 1
STA 2502 [A] -> [2502], Result
MOV A, C [A] <- [C]
STA 2503 [A] -> [2503], Borrow
HLT Stop
8085 Microprocessor Programs · Original code unchanged
22 / 24

## Slide 23
Subtract two 8-bit numbers with or without borrow
Explanation – Registers A, H, L, C are used for general purpose:
Explanation
MOV is used to transfer the data from memory to accumulator (1 Byte)
LHLD is used to load register pair directly using 16-bit address (3 Byte instruction)
MVI is used to move data immediately into any of registers (2 Byte)
STA is used to store the content of accumulator into memory(3 Byte instruction)
INR is used to increase register by 1 (1 Byte instruction)
JNC is used to jump if no borrow (3 Byte instruction)
SUB is used to subtract two numbers where one number is in accumulator(1 Byte)
HLT is used to halt the program
8085 Microprocessor Programs · Original code unchanged
23 / 24

## Slide 24
End of programs
All listings, comments, and explanations match the original text files in this repository.
8085 Microprocessor Programs · Original code unchanged
24 / 24